## Slide 1: IEEE PCB Design Workshop: (Week 01) Introduction to Schematics
<N
Hosted By: Adrian Sucahyo and IEEE at the University of Utah
Adapted From: IEEE x FSAE Workshop SP25 with Nick Howard and Adrian Sucahyo

## Slide 2
Workshop Outline
Tentatively scheduled for ~9 weeks
Sept. 3 – Introduction to Schematics
Sept. 10 – Schematics Continued
Sept. 17 – Introduction to PCB Layout
Sept. 24 – Layout Continued
Oct. 1 – Open Work Session
** FALL BREAK **
Oct. 22 – Soldering Week 1
Oct. 29 – Soldering Week 2
Nov. 5 – Soldering Week 3
Nov. 12 – Final Notes and Next Steps

## Slide 3
Workshop Logistics
We highly recommend attending all workshop sessions
  Each session is designed to build off previously discussed materials
By the end of the workshop, you will be able to:
  Build an adjustable USB-C Breadboard Power Supply
  Understand the basics of schematic layout, PCB layout, and board manufacturing
  Gain experience with through-hole and surface mount PCB assembly
  Have a basic understanding of manufacturing techniques and equipment used in the industry

## Slide 4
Workshop Logistics
We hope to not charge a fee for this workshop and supporting materials
  Tentative on ASUU funding for the Fall Semester
  Will know by October if fees will be necessary
Want to pursue a different project? Chat or Email Us!
  We may be able to support individual projects get board manufactured

## Slide 5
Want more experience?
Consider joining the FSAE tractive team!
  The Tractive Team is currently looking for students to assist with designing and assembling the electrical system for an electric formula-style race car!
  No experience required!

## Slide 6
Join the IEEE Discord
If you haven’t already, please join the IEEE Discord server for additional information and updates regarding this workshop

## Slide 7
What is a schematic?
Schematics are a graphical representation of an electrical circuit or system
  A step up from a block diagram
  Shows all parts and electrical connections in a circuit
  Used to route PCB traces during layout
Schematics are NOT a physical representation of component positions on the PCB

## Slide 8
Components in a Schematic
Every electrical component will have its own symbol within the schematic
  Contains all pins connected to the component
  May contain additional information such as signal type
  Relatively consistent across platforms
https://learn.sparkfun.com/tutorials/how-to-read-a-schematic/all

## Slide 9
Symbol Attributes
Symbols may have additional information regarding the component they represent
  Designators
  Values
  Part Numbers
  Pin Name
  Pin Number

## Slide 10
US vs International Symbols
You may see variations on certain components between US and International Schematics
  Resistors, Capacitors, Inductors and more may have slightly different schematic symbols
https://learn.sparkfun.com/tutorials/how-to-read-a-schematic/all

## Slide 11
Nets and Nodes
Schematic Nets are how components are electrically connected in a circuit
  Represented with lines between components
Nodes/Junctions are locations where wires split in two (or more)
  A connection on a node is denoted by a dot

## Slide 12
Net Labels
Net Labels allow electrical connections to be made without having to draw a line between components
  Net Labels tend to be local to the current schematic sheet
  Power Labels tend to be global to the full design
Note: Ports are similar but have a different purpose
  Useful for hierarchal / multi-sheet design

## Slide 13
Good Schematic Practice
Readability is KEY!
  The schematic needs to be read by other engineers to assist with layout and debugging
  Readable schematics make it easier to find electrical errors which would be translated into the physical layout
https://xkcd.com/730/

## Slide 14
Tips:
Read Left to Right
Don’t Overcrowd
  Use a larger sheet or use multi-sheet drawings
Use Logical Blocks to Divide Circuit Elements
Reference Manufacturer Datasheets
  Follow established layouts
Label Signals
  Especially those which are not immediately obvious
Keep Power Sources at the top and GND at the Bottom

## Slide 15
Examples:
From Nick Howard, Week01 IEEE x FSAE Workshop SP25

## Slide 16
ECAD Software
ECAD (Electronic Computer-Aided Design) are software used to design and create diagrams and layouts for PCBs
There are many different vendors for ECAD software:
  Altium
  KiCAD
  Eagle
  OrCAD
  EasyEDA

## Slide 17
Why Altium?
Altium is very commonly used in the industry for PCB and circuit assembly
Not many opportunities to get access to the software outside of university
  Please get your student license ASAP if you haven’t already
Great addition to your resume!

## Slide 18
Project Introduction
USB-C Breadboard Power Supply
  Dual Switching Supplies
    Independent Voltage Outputs
    Switch between isolated / tandem supplies
  Dual Input Supplies
    Primary and Secondary Supplies
    Terminal Block Input
  USB-C PD trigger on Primary Supply
    Additional Barrel Jack DC input
  Configurable output bleeder resistors

## Slide 19
Block Diagram
Block diagram drawn using draw.io

## Slide 20
Power Inputs and Input Selection
Power Inputs
  Terminal Block Input
  Barrel Jack Input
  USB-C PD Breakout
  20 VDC Max
Input Selection
  Select between a primary and secondary supply
  Isolate supply A and B for independent operation

## Slide 21
Switching Supplies
Texas Instruments Simple Switchers – LM2596
  Buck Converter
  Adjustable Output
  3 Amp Output Load Capacity
Reference Datasheet for more information and reference circuit
https://www.ti.com/product/LM2596

## Slide 22
Power Outputs
Power Outputs
  Terminal Block Output
  Pin Headers
  Breadboard width for easy utilization
Output Bleeder Resistors

## Slide 23
Questions?
Questions?

## Slide 24
Download Today’s Project Files
Navigate to the workshop GitHub and download today’s files https://github.com/IEEE-U-of-U/IEEE-PCB-Workshop-Fall-2025